## Slide 1: Fractional-Order Stochastic Extremum Seeking Control with Dithering Noise for Plasma Impedance Matching
The 2021 IEEE Conference on Control Technology and Applications (CCTA)
Jairo Viola1, Derek Hollenbeck1, Carlos Rodriguez2, and YangQuan Chen1
1MESA (Mechatronics, Embedded Systems and Automation)Lab
Mechanical Engineering, University of California, Merced
2Ensenada Center for Scientific Research and Higher Education, Mexico
E: (jviola, dhollenbeck, ychen53)@ucmerced.edu, crodriguez@cicese.edu.mx
08/08/2021, San Diego, California

## Slide 2: Outline
1
Introduction
2
3
L-Type network Plasma Impedance Matching
4
Conclusions and future works
Fractional-Order Extremum Seeking Control

## Slide 3: 1.Introduction
RF Plasma Impedance Matching
High variability plasma impedance
Unknown plasma dynamics
Complex physics model
Maximum power transfer is granted when
Reflection coefficient
Optimization goal

## Slide 4: 1.Introduction
Types of impedance matching:
Passive Impedance Matching
  Fixed loads
  Impedance adjusted by fixed capacitor or inductors
Automatic Impedance Matching
  Real-time varying capacitors
  PID control
  Gradient based
  Seeking algorithms (Magnitude and phase)
The impedance matching success is measured usually for a single and invariant load without considering performance criteria like:
Settling time
Reflected power coefficient
Convergence rate under different capacitor initial conditions and uncertain load

## Slide 5: 2. Fractional-Order Extremum Seeking Control
Integer-Order Sinusoidal Perturb and observe Extremum Seeking Control (IO P&O ESC)
Where:
cost function output, : minimum of
unknown optimal parameters, estimated value of , : parameter error
: amplitude and frequency of perturbing signal
Low pass filter frequency

## Slide 6: 2. Fractional-Order Extremum Seeking Control
Fractional-Order Perturb and observe Stochastic Extremum Seeking Control (FO P&O SESC)
D. Hollenbeck and Y. Chen, “A More Optimal Stochastic Extremum Seeking Control Using Fractional Dithering For A Class of Smooth Convex Functions,” 2020.
can be replaced by integer/fractional order gaussian noise
bounded noise
, unbounded noise
Fractional gaussian noise
Hurst parameter
Brownian motion
Positively correlated (LRD)
Negatively correlated (LRD)

## Slide 7: 3. L-Type network Plasma Impedance Matching
L-Type Network configuration
Component | Value | 
 | min | max
Component | Value | 
 | min | max

## Slide 8: 3. L-Type network Plasma Impedance Matching
L-Type Network configuration
Capacitor-space (starting capacitor positions) for L-Type network for given
Feasible matching region for L-Type network
Controllability challenge
Feasible matching

## Slide 9: 3. L-Type network Plasma Impedance Matching
MIMO FO/IO ESC controller for L-Type network
Motor dynamics ()
ESC cost
function

## Slide 10: 3. L-Type network Plasma Impedance Matching
Test 1: P&O ESC and FO-SESC for
Capacitor initial condition has significant influence over ESC convergence
Ten times simulation results average for five different IC
Performance indices: Settling time, convergence rate (), and Reflection coefficient RMS

## Slide 11: 3. L-Type network Plasma Impedance Matching
Test 1: P&O ESC and FO-SESC for and
Ten times simulation results average for five different IC
Performance indices: Settling time, convergence rate (), and Reflection coefficient RMS
Settling time
C (%)

## Slide 12: 3. L-Type network Plasma Impedance Matching
Test 2: P&O ESC and FO-SESC Controllers Global Convergence Analysis
Evaluate convergence for all the feasible load space
Ten times simulation results average for five different IC
Performance indices: Settling time, convergence rate, and Reflection coefficient RMS
Settling time
C (%)

## Slide 13: 3. L-Type network Plasma Impedance Matching
Test 2: P&O ESC and FO-SESC Controllers convergence region evolution
For the convergence region increases
Blue: success
Red: miss

## Slide 14: 3. L-Type network Plasma Impedance Matching
Test 3: ESC Controllers Capacitor Initial Condition Robustness Analysis
25 different loads against 25 initial conditions .
Ten times simulation results average
IC convergence space for
Total convergence rate for test 3
improves convergence rate

## Slide 15: 4. Conclusions and future work
A Perturb and Observe Fractional-Order Stochastic Extremum Seeking Control (P&O FO-SESC) with dithering noise was designed for plasma impedance matching.
Obtained results show that using a dithering noise in the P&O FO-SESC controller in the range can improve the system convergence rate, settling time, and minimize the total reflected power during the impedance matching process.
Obtained results show that using a dithering noise in the P&O FO-SESC controller in the range 0.5≤𝐻≤0.6 can improve the system convergence rate, settling time, and minimize the total reflected power during the impedance matching process.
As future works, the P&O FO-SESC controller design, simulation, and evaluation using the admittance model of the matching network instead of impedance is proposed based on Smith chart analysis. Likewise, introducing feedforward mechanisms based on magnitude and phase to improve ESC control performance can be considered.
The P&O FO-SESC controller is robust under different loads and capacitor initial conditions, indicating that the P&O FO-SESC controller is suitable for plasma impedance matching where plasma load impedance is time variant and unknown.
A L-Type network with two variable capacitors was employed to perform the matching control. The P&O FO-SESC controller was tested for single and multiple loads under different initial conditions and different levels of LRD on the dithering noise given by the Hurst exponent.
A Perturb and Observe Fractional-Order Stochastic Extremum Seeking Control (P&O FO-SESC) with dithering noise was designed for plasma impedance matching.
As future works, the P&O FO-SESC controller design, simulation, and evaluation using the admittance model of the matching network instead of impedance is proposed based on Smith chart analysis. Likewise, introducing feedforward mechanisms based on magnitude and phase to improve ESC control performance can be considered.
The P&O FO-SESC controller is robust under different loads and capacitor initial conditions, indicating that the P&O FO-SESC controller is suitable for plasma impedance matching where plasma load impedance is time variant and unknown.
A L-Type network with two variable capacitors was employed to perform the matching control. The P&O FO-SESC controller was tested for single and multiple loads under different initial conditions and different levels of LRD on the dithering noise given by the Hurst exponent.

## Slide 16: References
Y. F. Li, “Analysis and design of tracking control for the RF matching box of plasma system,” ACM International Conference Proceeding Series, pp. 18–23, 2019.
S. Ishida, A. Kawamura, A. Takayanagi, and H. Takada, “Robust convergence of the impedance matching process based on seek control,” IECON Proceedings (Industrial Electronics Conference), pp. 1554– 1559, 2011.
Y. Ma and G. Wu, “Automatic impedance matching using simulated annealing particle swarm optimization algorithms for RF circuit,” Proceedings of 2015 IEEE Advanced Information Technology, Electronic and Automation Control Conference, IAEAC 2015, pp. 581–584, 2016.
Y. Hirose, A. Kawamura, A. Takayanagi, and H. Takada, “Analysis of impedance matching control,” 2009 IEEE 6th International Power Electronics and Motion Control Conference, IPEMC ’09, vol. 3, pp. 1188–1191, 2009.
C. Zhang and R. Ordoñez, Extremum-Seeking Control and Applications, 1st ed. London: Springer-Verlag London, 2012. [Online]. Available: http://link.springer.com/10.1007/978-1-4471-2224-1
K. Bariyur and M. Krstic, Real-time optimization by extremum-seeking control. Wiley-Interscience, 2003.
S.-J. Liu and M. Krstic, Stochastic Averaging and Stochastic Extremum Seeking. Springer, 2013, vol. 53, no. 9.
C. Yin, Y. Chen, and S. M. Zhong, “Fractional-order sliding mode-based extremum seeking control of a class of nonlinear systems,” Automatica, vol. 50, no. 12, pp. 3173–3181, 2014. [Online]. Available: http://dx.doi.org/10.1016/j.automatica.2014.10.027
D. Hollenbeck and Y. Chen, “A more optimal stochastic extremum seeking control using fractional dithering for a class of smooth convex functions,” in 2020 IFAC World Congress, 2020, pp. 1–6.
P. Dix, B. Ashrafi, S. Drakunov, and U. O¨ zguner, “ABS Control Using Optimum Search via Sliding Modes,” IEEE Transactions on Control Systems Technology, vol. 3, no. 1, pp. 79–85, 1995.
G. A. Frantsuzova, “Use of a Relay Controller for Automatic Extremum Seeking in Nonlinear Systems,” Avtometriya, vol. 47, no. 3, pp. 274–280, 2011.
R. L. Magin, “Fractional calculus in bioengineering.” Critical reviews in biomedical engineering, vol. 32, no. 1, pp. 1–104, 2004.
H. Sheng, Y. Chen, and T. Qiu, Fractional Processes and Fractional- Order Signal Processing Techniques and Applications. Springer, 2012

## Slide 17
Thanks for your attention!