## Slide 1: Unmanned Autonomous Systems: A Tutorial (Part 1)
YangQuan Chen, Ph.D., Director,
MESA (Mechatronics, Embedded Systems and Automation)Lab
ME/EECS/SNRI/HSRI/UCSolar, School of Engineering,
University of California, Merced
E: yqchen@ieee.org; or, yangquan.chen@ucmerced.edu
T: (209)228-4672; O: SE2-273; Lab: CAS Eng 820 (T: 228-4398)
July 30, 2016. Saturday
东北大学2016人工智能与机器人国际暑期学校
Northeastern University, China

## Slide 2: Acknowledgement
Prof. Chengdong Wu for the invitation
This lecture module is based on IFAC 2008 World Congress tutorial paper/slides by Kevin L. Moore
  “A Tutorial Introduction to Autonomous Systems,” Kevin L. Moore, Proceedings of 2008 IFAC World Congress, pp. 11720-11731, Seoul, Korea. July 2008 (invited Keynote paper for Invited Session on Intelligent Autonomous Systems).

## Slide 3: Outline/Miniplan
Part 1: CSOIS Ground Mobile Robots (unmanned autonomous systems/vehicles)
Part 2: UAS (unmanned aircraft systems)
Part 3: Future Robotics Research: From CPS to CHS

## Slide 4: Skip Ad in 1 minutes

## Slide 5: University of California, Merced
The Research University of the Central Valley
Centrally Located
  Sacramento – 2 hrs
  San Fran. – 2 hrs
  Yosemite – 1.5 hrs
  LA – 4 hrs
Surrounded by farmlands and sparsely populated areas

## Slide 6: UC Merced
Established 2005
1st research university in 21st century in USA.
5,764 Undergraduates
442 Grads (90% Ph.Ds)
Strong Undergraduate Research Presence (HSI, MSI)

## Slide 7: The MESA Lab
Mechatronics, Embedded Systems, Automation Lab
http://mechatronics.ucmerced.edu
Lab Director: Prof. YangQuan Chen
  Lab Manager: Brandon Stark
  6 Ph.D. Students
  40+ Undergrads
  9 Visiting Ph.D. Students
  6 Visiting Professors/Scholars
Unmanned Aerial Systems
Cyber-Physical Systems
Renewable Energy Systems
Mechatronic Systems
Applied Fractional Calculus

## Slide 8
Scientific
Data Drone Valley

## Slide 9: MESA Research Areas/Strengths
Unmanned Aerial Systems and UAV-based Personal Remote Sensing (PRS)
Cyber-Physical Systems (CPS)
Modeling and Control of Renewable Energy Systems
Mechatronics
Applied Fractional Calculus (AFC)

## Slide 10: Overview
Purpose of paper is to present a
  tutorial-level introduction to the technical aspects of unmanned autonomous systems.
We emphasize
  a system engineering perspective on the conceptual design and integration of both
    the components used in unmanned systems including the locomotion, sensors, and computing systems needed to provide inherent autonomy capability, and
    the algorithms and architectures needed to enable control and autonomy, including path-tracking control and high-level planning strategies.
Concepts are illustrated using case study examples from robotic and unmanned system developed by the author and his colleagues

## Slide 11: Acknowledgments
Professor D. Subbaram Naidu
Idaho State University
Measurement and Control Engineering Research Center
Professor YangQuan Chen
Professor Nicholas Flann
Utah State University (USU)
Center for Self-Organizing and Intelligent Systems (CSOIS)
Mr. Mel Torrie
Autonomous Solutions, Inc.
David Watson
David Schiedt
Dr. I-Jeng Wang
Dr. Dennis Lucarelli
Johns Hopkins Applied Physics Lab (APL)
ALL MY STUDENTS OVER THE YEARS!
Autonomous Solutions, Inc.™

## Slide 12: Outline
  What is an Unmanned System?
  Unmanned system components
    Motion and locomotion
    Electro-mechanical
    Sensors
    Electronics and computational hardware
  Unmanned system architectures and algorithms
    Multi-resolution approach
    Software Architecture
    Reaction, adaptation, and learning via high-level feedback

## Slide 13: Unmanned Systems
What is an unmanned system?
What is an unmanned vehicle?
Is an unmanned system a robot?
Is a robot an unmanned system?
Is an unmanned system an autonomous system?
What about unmanned sensors?
What about mobile sensors?
What about telepresense or tele-operation?
What about teams of unmanned vehicles, or swarms?
DARPA Crusher 1.0

## Slide 14: Unmanned System
Let us define:
  Unmanned system: any electro-mechanical system which has the capability to carry out a prescribed task or portion of a prescribed task automatically, without human intervention
  Unmanned vehicle: a vehicle that does not contain a person
    Can be tele-operated
    Can be autonomous
    Typically deploys a payload (sensor or actuator)
Focus today will be on unmanned vehicles
Unmanned vehicles can come in several flavors: UxV
  Land: UGV
  Air: UAV
  Maritime: UUV, USV
  Sensors: UGS

## Slide 15: What Makes a UxV?
All UxVs have common elements:
  Mechanical components (drive, power, chassis)
  Electronics
  Sensing/mission payloads
  Communication systems
  Control
  “Smarts”
  Interface to user
Our perspective is that all unmanned systems should be developed from the perspective of its concept of operations (CONOPS)

## Slide 16
Example CONOPS - Automated Tractors
Example CONOPS -Unique Mobility Robots (Autonomous Solutions, Inc.)

## Slide 17: What Makes a UxV?
All UxVs have common elements:
  Mechanical components (drive, power, chassis)
  Electronics
  Sensing/mission payloads
  Communication systems
  Control
  “Smarts”
  Interface to user
Our perspective is that all unmanned systems should be developed from the perspective of its concept of operations (CONOPS)
Once a CONOPS has been defined, then systems engineering is used to flow-down requirements for subsystems.

## Slide 18
We consider two key aspects of unmanned vehicles and autonomy:
  Inherent physical capabilities built into the system
  Intelligent control to exploit these capabilities
Inherent physical capabilities
  Mechanisms for mobility and manipulation
  Power
  Sensors for perception
    Proprioceptive
    External
  Computational power
Intelligent control to exploit these capabilities
  Machine-level control
  Perception algorithms
  Reasoning, decision-making, learning
  Human-machine interfaces
These are driven by
your CONOPS
These are driven by
your CONOPS, but also by your inherent physical capabilities
Unmanned Systems: Capabilities and Control

## Slide 19: Case Study/Illustrative Example
In following, we discuss
  Inherent capability in unmanned ground systems
  Exploitation of these inherent capabilities
Primarily use the Omni-Directional Inspection System (ODIS) as a case study
  Inherent capability in ODIS
  Exploitation of these inherent capabilities

## Slide 20
ODIS I – An Autonomous Robot Concept

## Slide 21: Outline
  What is an Unmanned System?
  Unmanned system components
    Motion and locomotion
    Electro-mechanical
    Sensors
    Electronics and computational hardware
  Unmanned system architectures and algorithms
    Multi-resolution approach
    Software Architecture
    Reaction, adaptation, and learning via high-level feedback
  Toward an algorithmic framework for autonomous UxVs

## Slide 22: UGV Technology
Motion

## Slide 23: Motion and Locomotion for Unmanned Systems
Except for UGS, most unmanned systems must move:
UGV: wheels and tracks
UAV: fixed wing, rotary wing, VTOL
USV/UUV: propeller based, jetted
In general the motion and locomotion aspects of an unmanned vehicle are not remarkably different than that of their manned counterparts:
  Design of motion and locomotion system becomes “only” an engineering task!

## Slide 24: Some ODV Robots Built At USU
T1 -1998
T2 -1998
ODIS I -2000
T3 -1999
T4 -2003
(Hydraulic drive/steer)
Typical UGV Mobility Platforms
    Ackerman
    Skid-Steer
    Unicycle
    Unique Mobility

## Slide 25
Mobility Example: USU ODV Technology
USU developed a mobility capability called the “smart wheel”
Each “smart wheel” has two or three independent degrees of freedom:
  Drive
  Steering (infinite rotation)
  Height
Multiple smart wheels on a chassis creates a “nearly-holonomic” or omni-directional (ODV) vehicle

## Slide 26
T1 Omni Directional Vehicle (ODV)
Smart wheels make it
possible to simultaneously
- Translate
- Rotate
ODV steering gives improved mobility compared to
conventional steering

## Slide 27
T2 Omni Directional Vehicle
T2 can be used for military scout
missions, remote surveillance, EOD,
remote sensor deployment, etc.

## Slide 30
Omni-Directional Inspection System (ODIS)
First application of ODV technology
Man-portable physical security mobile robotic system
Remote inspection under vehicles in a parking area
Carries camera or other sensors
Can be tele-operated, semi-autonomous, or autonomous

## Slide 31
“Putting Robots in Harm’s Way So People Aren’t”
ODIS – the Omni-Directional Inspection System
An ODV Application: Physical Security
Under joystick control

## Slide 32
ODIS On Duty in Baghdad
“Putting Robots in Harm’s Way, So People Aren’t”

## Slide 33
Systems Engineering a UGV: Case Study
ODIS Design and Implementation

## Slide 34: Overall Specifications
Weight: approx. 40 lb.
Height: 3.75 inches
Footprint: 25” X 32”
Velocity: 2.5 ft/sec
Power Source: Battery
Number of Wheels: 3
Number of Processors: 8
Environmental Sensing: Sonar, IR, Laser
Position Sensing: dGPS, FOG
Vehicle Runtime: 1 Hour
Number of Battery Packs: 2 (12 V and 24 V)
Ground Clearance: 0.5 inches

## Slide 35: Steering Characteristics
24 Volt Maxon 110125 Motor
98:1 Gear Reduction
Integrated 6 Contact Custom
Slipring Assembly
Steering Rate of 1 rev/sec max.
Overall Weight = 3.24 lb.
Computer Optics 10 bit Absolute
Encoder

## Slide 36: ODIS Steering Layout
BEARING
BELT PULLEYS
SLIPRING
ASSEMBLY
ABSOLUTE ENCODER
STEERING MOTOR
& GEARHEAD
DRIVE ASSEMBLY
CHASSIS ATTACHMENT

## Slide 37: Drive Characteristics
QT 1221A 17 Volt Kollmorgen Frameless Torquer Motor
43:1 Micro-Mo Gearbox
2.6 Feet/Second Top Speed
25 Pounds Max Drive Force Per Wheel
80 mm Wheel Diameter
CUI Stack Incremental Encoder

## Slide 38: Power for Unmanned Systems
Power for UxVs is one of today’s limiting issues.
Battery-based systems
  Lead-acid
  Nickel-Metal Hydride
  Lithium-Ion
  Silver-Zinc
Combustion-engines
  Gasoline
  Diesel
Fuel cells
Novel: wind/water
Fuel-cell powered ODIS developed by Kuchera Defense Systems
Station-keeping sailboat

## Slide 39: ODIS Battery Assembly
Guide Block
Battery Clip
12V NiMH Battery
Contacts

## Slide 40: UGV Technology
Chassis
Motion

## Slide 41
ODIS Chassis Layout
STEERING/DRIVE
ASSEMBLIES
LASER
FIBER OPTIC
GYRO
PAN/TILT
CAMERA
BATTERY PACKS
VETRONICS
1/16” Aluminum Panels
Glued & Riveted on Joints
Interior Shear Panels

## Slide 42: UGV Technology
Ve-Tronics
Chassis
Smart
Wheel

## Slide 43: Vetronics Block Diagram
Joystick
Video
Display
Video
TX
Camera
Node
Vehicle
GUI
Planner
GUI
LAN
RF
Modem
PPP
RF
Modem
Planner
Node
Master Node
(SBC)
GPS
Off-board Vehicle
Wheel Node
(x 3)
IR
Sensor
Nodes
FOG
Laser
Sonar
Sensor
Node
Vetronics Overview

## Slide 44: Master Node
LPT1
RS-232 (x4)
Connect Tech
D-Flex 8
RS-232/RS-485
RS-485 (x3)
PC104
Freewave
900Mhz
Modem
Cell 233 MHz PC Card
with PC-104 Stack
COM3-RX
Master Node
2.5”
HDD
COM1
Freewave
900Mhz
Modem
10BaseT
Joystick
Command Modem
Path Planner
PPP Modem
LAN
COM2
Wheel Nodes (x3)
Laser Range finder
IR Sensor Nodes (2)
Sonar Sensor Node
Camera Node
COM3 TX
COM4
Sync
Reset
RS-485
FOG
dGPS
Master Node Subsystem

## Slide 45: Wheel Node Block Diagram
RS232
Debug
Port
RS232
RS232
MC68332
Microcontroller
(TT8)
SPWM
SDIR
DPWM
DDIR
CHB
CHA
Computer
Optical Products
10-Bit Absolute Enc.
Absolute
Encoder
Interface
Hardware
Watchdog
Motor Driver
PCB
Advanced Motion
Controls
10A8DD
Motor Driver
LMD18200T
Motor Driver
2
Steering
Motor
2
Drive
Motor
Wheel
Master
Interface
10
Steering
Angle
Quadrature
Encoder
RS485
Tx-Rx
Reset
Sync
Enable
Wheel Node Subsystem

## Slide 46: Vehicle Power System
12V
NiMH
12V
NiMH
12V
NiMH
12V
NiMH
External
12V
Power
24V Power
Distribution PCB
Laser
Battery
Power
Latch
Reset
Wheel
Vectronics
24V
Power
Fuses
Switch Interface
DC-DC
Converters
Power System
Fuses
12V BUS
24V-Laser
12V Wheels
24 Volt
Motor
Drivers
12V Power
Distribution
PCB
24V
Power
Relays
FOG
GPS
IR Sensor
Node
(2)
Sonar
Sensor
Node
Camera
Node
12V M
Master
Computer
Carrier Board
Freewave
Modem
Freewave
Modem

## Slide 47: ODIS Weight Budget
BATTERY PACKS
PAN/TILT
CAMERA ASSEMBLY
LASER
IR SENSORS
SONAR SENSORS
Chassis = 11.28 lbs
Vetronics = 9.53 lbs
Drive/Steering = 14.11 lbs
Batteries = 5.80 lbs
ODIS = 40.72 lbs
900 MHz
ANTENNAS
GPS ANTENNA

## Slide 48: ODIS Vetronics System

## Slide 49: UGV Technology
Sensors
Ve-Tronics
Chassis
Smart
Wheel

## Slide 50: ODIS Sensor Suite
Sonar Board
IR Boards
Laser
Sonar
IR
Camera
Camera Board

## Slide 51
B
E
A
M
P
A
T
T
E
R
N
|
IR
|
Sonar
|
Laser

## Slide 52
Sensors and Safety: Automated Tractor Project Example

## Slide 53: Safety Scenarios
We need to halt the vehicle if:
  Tractor leaves field boundary or deviates from path
  Unavoidable obstacle within given threshold
  Communication disrupted or lost
  d-GPS dropout corrupts position information
  Computer failures occur
  Emergency stop button
  Vehicle halt computer command
  Mission complete
Some safeguards include
  Sensor suite for detecting vehicle path obstructions
  Redundant radio link to protect against wireless communication dropout or corruption.
  Use of odometry to complement/supplement dGPS

## Slide 54
Awareness Issues

## Slide 55: 3 Tiered Proximity Detection
d
Hazard zone
Pressure Bumper
Radar
Ultrasonic/IR
30’

## Slide 56: Localization Issues
Poor Radio Communications
  High power antennas
  Lower Frequency
Intermittent GPS
  Dead-reckoning
  Reactive positioning
    Hole-following with range data
    Row sensing with laser

## Slide 57: Mission Payloads for UxVs
Different CONOPS will produce different mission payload requirements.
ODIS-T Sensor Suites:
  Visual – pan/tilt imaging camera
  Passive & active thermal imaging
  Chemical sniffers – i.e. nitrates, toxic industrial chemicals
  Night vision sensors
  Acoustic sensors
  Radiation detectors – i.e. dirty bombs
  Biological agents detection
  MEMS technology – multiple threats
  License plate recognition

## Slide 58: Mission Packages - IR
IR Image – Warm Brake
IR Image – Recently Driven Vehicle
Notes: If we view the underside of a cold vehicle with an IR camera, we see some indication of the vehicles components, but very little stands out. We do see some hot spots, in this case a tire warmed by the sun. Bases on telemetry from the ODIS robot compass and a time of day clock, we can determine that this is the likely case. If the opposite tire had been showing as a hot spot, this should be flagged as an anomaly and the inspector alerted via the OCU. A recently arrived vehicle has a different signature than a cold vehicle. In this case, the brakes and wheel rim are radiating thermal energy (Figure 9a), the exhaust system is glowing brightly and the differential is also glowing, although less brightly (Figure 9b). This indicates a very recently arrived vehicle. As the parked vehicle cools, the exhaust system will cool faster than the much more massive differential. By comparing the intensity of components, we can determine approximately how long the vehicle has been in place and make appropriate decisions.

## Slide 59: Mission Payloads for UxVs
Different CONOPS will produce different mission payload requirements
ODIS-T Sensor Suites:
  Visual – pan/tilt imaging camera
  Passive & active thermal imaging
  Chemical sniffers – i.e. nitrates, toxic industrial chemicals
  Night vision sensors
  Acoustic sensors
  Radiation detectors – i.e. dirty bombs
  Biological agents detection
  MEMS technology – multiple threats
  License plate recognition
Mission payload can be actuators as well as sensors
Samsung Robot Sentry

## Slide 60: UGV Technology
Mission Planning
Path Tracking Control
Sensors
Ve-Tronics
Chassis
Smart
Wheel

## Slide 61: Outline
  What is an Unmanned System?
  Unmanned system components
    Motion and locomotion
    Electro-mechanical
    Sensors
    Electronics and computational hardware
  Unmanned system architectures and algorithms
    Multi-resolution approach
    Software Architecture
    Reaction, adaptation, and learning via high-level feedback

## Slide 62: Multi-Resolution Control Strategy
At the lowest level:
  Actuators run the robot
Mission Planner
Robot Dynamics
Path-Tracking
Controllers
Low-Level
Controllers
Highest
Bandwidth
(20 Hz)
Command Units
Low
Bandwidth
(1 Hz)
Actuator Set-points
Medium
Bandwidth
(10 Hz)
Voltage/Current

## Slide 63: Multi-Resolution Control Strategy
At the middle level:
  The path tracking controllers generate set-points (steering angles and drive velocities) and pass them to the low level (actuator) controllers
Mission Planner
Robot Dynamics
Path-Tracking
Controllers
Low-Level
Controllers
Highest
Bandwidth
(20 Hz)
Command Units
Low
Bandwidth
(1 Hz)
Actuator Set-points
Medium
Bandwidth
(10 Hz)
Voltage/Current

## Slide 64: Multi-Resolution Control Strategy
Mission Planner
Robot Dynamics
Path-Tracking
Controllers
Low-Level
Controllers
Highest
Bandwidth
(20 Hz)
Command Units
At the highest level:
  The mission planner decomposes a mission into atomic tasks and passes them to the path tracking controllers as command-units
Low
Bandwidth
(1 Hz)
Actuator Set-points
Medium
Bandwidth
(10 Hz)
Voltage/Current

## Slide 65
  Behavior Generation Strategies
First Generation: pre-T1
  Waypoints fit using splines for path generation
  User-based path generation
Second Generation: T1, T2
  decomposition of path into primitives
  fixed input parameters
  open-loop path generation

## Slide 66
  Behavior Generation Strategies
First Generation: pre-T1
  Waypoints fit using splines for path generation
  User-based path generation
Second Generation: T1, T2
  decomposition of path into primitives
  fixed input parameters
  open-loop path generation
Third Generation: T2, T3, ODIS
  decomposition of paths into primitives
  variable input parameters that depend on sensor data
  sensor-driven path generation

## Slide 67
  3rd Generation Maneuver Command:
  Sensor-Driven, Delayed Commitment Strategy
  (ALIGN-ALONG (LINE-BISECT-FACE CAR_001) distance)

## Slide 68
ODIS Command Environment: MoRSE
Based on command unit:
  Set of individual commands defining various vehicle actions that will be executed in parallel
Commands for XY movement:
  moveAlongLine(Line path, Float vmax, Float vtrans = 0)
  moveAlongArc(Arc path, Float vmax, Float vtrans = 0)
Commands for Yaw movement:
  yawToAngle(Float angle_I, Float rate = max)
  yawThroughAngle(Float delta, Float rate = max)
Commands for sensing:
  SenseSonar – SenseIR
  SenseLaser – Camera commands
A set of rules defines how these commands may be combined

## Slide 69
Software Architecture
Command actions are the lowest-level tasks allowed in our architecture that can be commanded to run in parallel
For planning and intelligent behavior generation, higher-level tasks are defined as compositions of lower-level tasks
In our hierarchy we define:
Variable (planned)
Hard-wired (but,
(parameterized and
sensor-driven)
User-defined
Mission
Tasks
Subtasks
Atomic Tasks (Scripts)
Command Units
Command Actions

## Slide 70
Environment
External
Internal
External
Internal
User Input
Mission
Actions
Events
IR
Camera
wheels
GUI Communicator
Awareness
Localize
Sonar
Laser

## Slide 71
01
02
03
04
05
06
07
08
09
10
11
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
46
47
48
49
50
51
52
53
54
55
56
57
58
59
60
61
62
63
64
65
66
67
68
12
13
14
15
16
17
18
40
41
42
43
44
45
Robot’s Home
- Curbs
- Lamp Posts
1 thru’ 68 - Stall Numbers

## Slide 72: User-tasks in the environment
{MoveTo Point}
{Characterize a stall}
{Inspect a stall}
{Characterize a row of stalls}
{Inspect a row of stalls}
{Localize}
{Find my Car}
{Sweep the parking lot}
{Sweep Specific area of the parking lot}

## Slide 73
Environment
External
Internal
External
Internal
User Input
Mission
Actions
Events
IR
Camera
wheels
GUI Communicator
Awareness
Localize
Sonar
Laser

## Slide 74
Environment
World
Database
External
Internal
External
Internal
User Input
Mission
Actions
Events
IR
Camera
wheels
Actuators
GUI Communicator
Awareness
Localize
Sonar
Laser
Sensors
Supervisory
Task Controller
Queries & updates
Updated Environment
Knowledge
Task
States and results of
atomic tasks execution
WD

## Slide 75
Supervisory
Task Controller
Environment
World
Database
External
Internal
External
Internal
User Input
Mission
Queries & updates
Updated Environment
Knowledge
Actions
Events
IR
Camera
wheels
Actuators
Optimization &
Ordering Module
Un-optimized
group of tasks
Ordered
group of tasks
GUI Communicator
Awareness
Localize
WD
Sonar
Laser
Sensors
Task
States and results of
atomic tasks execution

## Slide 76
Behavior Generator &
Atomic-Task Executor
Supervisory
Task Controller
Optimization &
Ordering Module
Environment
World
Database
External
Internal
External
Internal
User Input
Mission
Un-optimized
group of tasks
Ordered
group of tasks
Queries & updates
Updated Environment
Knowledge
Actions
Events
IR
Camera
wheels
Actuators
Resources
Ordered group
of Sub-tasks &
Atomic-tasks
Task
GUI Communicator
Awareness
Localize
WD
Sonar
Laser
Sensors
Task
States and results of
atomic tasks execution
Command-Units
Joy-stick
E-Stop

## Slide 77
Behavior Generator &
Atomic-Task Executor
Supervisory
Task Controller
Optimization &
Ordering Module
Environment
World
Database
External
Internal
External
Internal
User Input
Mission
Un-optimized
group of tasks
Ordered
group of tasks
Queries & updates
Updated Environment
Knowledge
Actions
Events
IR
Camera
wheels
Actuators
Resources
Ordered group
of Sub-tasks &
Atomic-tasks
Task
GUI Communicator
Awareness
Localize
WD
Sonar
Laser
Sensors
Sensor
Processor
Task
States and results of
atomic tasks execution
Command-Units
Observed input
Predicted changes
in the environment
Filtered &
Perceived input
Joy-stick
E-Stop
World Model
Predictor

## Slide 78
Supervisory
Task Controller
Behavior Generator &
Atomic-Task Executor
Optimization &
Ordering Module
Environment
Sensor
Processor
World
Database
External
Internal
External
Internal
User Input
Mission
Un-optimized
group of tasks
Ordered
group of tasks
Queries & updates
Updated Environment
Knowledge
Task
States and results of
atomic tasks execution
Actions
Command-Units
Events
Observed input
Predicted changes
in the environment
Filtered &
Perceived input
IR
Camera
wheels
Actuators
Control Supervisor (CS)
Command Actions
Resources
Ordered group
of Sub-tasks &
Atomic-tasks
Task
Joy-stick
E-Stop
GUI Communicator
Awareness
Localize
WD
Sonar
Laser
Sensors
World Model
Predictor

## Slide 79
Reactive Behaviors
Reactive behaviors are induced via:
Localization thread
  Compares expected positions to actual sensors data and makes correction to GPS and odometry as needed
Awareness thread
  Interacts with the execution thread based on safety assessments of the environment

## Slide 81
Awareness Thread

## Slide 82
Reactive Behaviors
Reactive behaviors are induced via:
Localization thread
  Compares expected positions to actual sensors data and makes correction to GPS and odometry as needed
Awareness thread
  Interacts with the execution thread based on safety assessments of the environment
Logic within the execution thread
  Scripted adaptive behaviors

## Slide 83
T2 Adaptive/Reactive Hill-Climbing

## Slide 84
Reactive Behaviors
Reactive behaviors are induced via:
Localization thread
  Compares expected positions to actual sensors data and makes correction to GPS and odometry as needed
Awareness thread
  Interacts with the execution thread based on safety assessments of the environment
Logic within the execution thread
  Scripted adaptive behaviors
  Exit conditions at each level of the hierarchy determine branching to pre-defined actions or to re-plan events

## Slide 86
Example: ODIS FindCar() Script

## Slide 87: Outline
  What is an Unmanned System?
  Unmanned system components
    Motion and locomotion
    Electro-mechanical
    Sensors
    Electronics and computational hardware
  Unmanned system architectures and algorithms
    Multi-resolution approach
    Software Architecture
    Reaction, adaptation, and learning via high-level feedback